## Slide 1: CSE 350 Digital Electronics and Pulse Techniques
Prerequisite:
Electronic Devices and Circuits,
Digital Logic Design
Mail: shomen.kundu@bracu.ac.bd
Desk: #4N148 Course Instructor: Shomen Kundu (SDU)

## Slide 2: Marks Distribution
Attendance : 2
Assignment : 5
Quiz : 18
Lab : 25
Midterm : 25
Final : 25
_____________________
Total : 100

## Slide 3: Syllabus ( Fall 25 )

## Slide 4: Timeline

## Slide 5: Review ( Circuits and Electronics )
Ohm’s law
KCL
KVL
Node Analysis

## Slide 6: Review ( Circuits and Electronics )
VA
VB
I
VA > VB
Ohm’s Law: In a fixed temperature the current flows through a conductor is proportional to the voltage difference across the conductor.

## Slide 7: Review ( Circuits and Electronics )
Node : Interconnected points between two and more electrical component.

## Slide 8: Review ( Circuits and Electronics )
Kirchhoff’s current law (KCL): states that the algebraic sum of currents entering a node (or a closed boundary) is zero.
Convention: a. Current Entering a node is positive
b. Current Exiting a node positive

## Slide 9: Review ( Circuits and Electronics )
Kirchhoff’s voltage law (KVL) states that the algebraic sum of all volt ages around a closed path (or loop) is zero.

## Slide 10: Review ( Circuits and Electronics )
Example: Find the value of I for the below circuit.
i

## Slide 11: Review ( Circuits and Electronics )
Node Analysis: Goal -> Finding “node voltage”
Techniques -> KCL and Ohm’s Law
Step:
Identify reference voltage
Identify unknown node voltage
Write the node equation
Solve the node equation

## Slide 12: Review ( Circuits and Electronics )
Example: Find the voltage of the node a. Given , and .
a

## Slide 13: Op-Amp Review
Important terminals of Op-Amp
 Non-Inverting ( Positive ) input terminal
 Inverting ( Negative ) input terminal
 Higher power supply terminal
 Lower power supply terminal
 Output terminal

## Slide 14: Op-Amp Review
Operational Amplifier can be used for different configurations
Open Loop  Comparator, Used in ADC
Negative Feedback Amplifier, Used in DAC
Positive Feedback  Signal generator, Schmitt Trigger

## Slide 15: Op-Amp Review
For open loop configuration
For ideal Op-Amp